#### Questions: Tannenbaum & Bos 1.{17,22,24,25}
17. What is a trap instruction? Explain its use in operating systems.
Executed to switch from user mode to kernel mode and start execution at fixed address in kernel. Similar to the procedure-call instruction because the following is a distant location and the return address is saved on the stack for later use. Trap instruction switches to kernel mode, where as a procedure-call does not change mode. Procedure-call gives relative address, Trap instruction cannot jump to an arbitrary address. Trap either jumps to a single fixed location or 8bit field containing jump address. Kernel code following trap dispatches to system call handler which then runs. Procedure call returns to caller. User call must clean stack.
22. Can the
count = write(fd, buffer, nbytes);
call return any value in count other than nbytes? If so, why?
On success nbytes is returned. On error, -1 is returned, and errno is set up appropriately. If count is zero and file descriptor refers to a regular file, 0 may also be returned.
24. Suppose that a 10-MB file is stored on a disk on the same track (track 50) in consecutive
sectors. The disk arm is currently situated over track number 100. How long will
it take to retrieve this file from the disk? Assume that it takes about 1 ms to move the
arm from one cylinder to the next and about 5 ms for the sector where the beginning of
the file is stored to rotate under the head. Also, assume that reading occurs at a rate of
200 MB/s.
I am not sure about this one, here is a guess:
(1ms*50tracks + 5ms) +10MB/200MB/s = 55ms + 0.5s = 555ms
25. What is the essential difference between a block special file and a character special
file?
Block special file provide access to device that transfers in groups of a fixed size, like a disk. A character special file provides access to device that increments a single character at a time, for example a terminal. Block special files have numbered blocks that can read/write independently. It is not possible to seek any block with character special files.